## Slide 1: Wood Manufacturing & Finishing Percentage of Quantities
Phase 6
Lecturer Jennifer Byrne

## Slide 2: Percentage of Quantities
The individual amounts of different materials in a mixture are stated in percentage form.
This is to ensure that when different quantities of a mixture are required they will be identical in composition.
After calculations the total must be the same as the whole number or add to 100%.

## Slide 3: Percentage of Quantities
E.g. A mixture of paint contains 85% white paint, 9% red paint and the remainder is blue.
What percentage of the paint is blue?
85 + 9 = 94
100 – 94 = 6 6% blue paint
Part 2
If we were told that the tin of paint weighed 2.5Kgs calculate the weight of each colour
White 85% of 2.5Kgs = 2.125Kgs 85% x 2.5 = 2.125
Red 9% of 2.5Kgs = 0.225Kgs 9% x 2.5 = 0.225
Blue 6% of 2.5Kgs = 0.150Kgs 6% x 2.5 = 0.150
2.500Kgs

## Slide 4: Percentage of Quantities
Moisture content in timber is expressed in percentage terms eg 20%MC
The percentage moisture content in timber is determined by comparing the weight of the moisture in a sample of timber to the dry weight of the same sample when dried
E.g. If the wet weight of a sample of timber is 35kgs and the dry weight is 29kgs find the moisture content
Wet weight – dry weight x 100 = MC% dry weight
35 – 29 x 100 = 6 x 100 = 20.7% 29 29
Answer is 20.7%MC

## Slide 5: Answers to Percentage of Quantities
Q1. An alloy contains 58% of zinc by weight and the remainder is copper. Calculate the weight of copper in 23kgs of the alloy.
100 – 58 = 42% copper is 42% of the weight
23 x 42% = 9.66kgs
Q2. A bronze statue contains 70% copper, 20% lead and the rest is tin. Find the weight of each metal in 165.8Kgs of bronze.
Copper 70% of 165.8Kgs = 116.06Kgs
Lead 20% of 165.8Kgs = 33.16Kgs
Tin 10% of 165.8Kgs = 16.58Kgs

## Slide 6: Answers to Percentage of Quantities
Q3. An alloy contains 2/5 of zinc by weight and the remainder is copper. Calculate the weight of copper in 70kgs of the alloy
As fractions copper is 3/5 70 x 3= 42Kgs 5
As percentages 60% 70 x 0.6 = 42kgs

## Slide 7: Answers to Percentage of Quantities
Q4. If the wet weight of a sample of timber is 36kg and the dry weight is 27kg find the moisture content
36 – 27 x 100 = 9 x 100 = 33.3% 27 27
33.3%M.C
Q5. If a wet sample of timber is 6.65kg and after being dried in the oven it weighs 5.35kg. Calculate the moisture content.
6.65 – 5.35 x 100 = 1.3 x 100 = 24.3% 5.35 5.35
24.3% M.C.

## Slide 8: Answers to Percentage of Quantities
Q6. A dry brick weighs 3.25kg and 4.0kg when totally saturated. Calculate the percentage porosity of the brick.
4.00 – 3.25 x 100 = 0.75 x 100 = 23% 3.25 3.25
23% porosity