## Slide 1: Wood Manufacturing & Finishing Ratio
Phase 6
Lecturer Jennifer Byrne

## Slide 2: Ratio
A ratio is a comparison of two numbers.
If there were 30 chairs in a room 12 were red and 18 were blue you would say that the ratio of red chairs to blue chairs was 12 to 18.
Ratio can be expresses in a number or ways:
12 to 18
12:18

## Slide 3: Ratio
Calculating falls and rises
E.g: If a flat roof has a fall of 1:38 and a span of 3.6m calculate the rise of the roof.
This will mean that for every 38 mm you go across you rise 1mm.
3600 ÷ 38 = 94.73
94.73mm = rise

## Slide 4: Ratio
Calculating falls and rises
E.g: If a flat roof has a fall of 1:38 and a span of 3.6m calculate the rise of the roof.
This will mean that for every 38 mm you go across you rise 1mm.
3600 ÷ 38 = 94.73
94.73mm = rise

## Slide 5: Ratio to calculate rise or fall
Q1. If a flat roof has a fall of 1:40 and a span of 3m calculate the rise of the roof.
Answer
3000 ÷ 40 = 75
75mm = rise
Q2. A sewerage pipe is laid with a fall of 1:20. Calculate the fall of the pipe over 4m.
Answer
4000 ÷ 20 = 200
200mm = fall

## Slide 6: Using ratios to solve problems
Example: €300 is divided between Alan & John in the ratio of 3:2.
To solve this type of question you must add together the numbers in the ratio to find how many parts there are, divide by the number of parts to find the value of 1 part, then multiply by the number of parts you want to calculate.
First add together the number of parts in the ratio: 3 + 2 = 5
Divide to find out how much 1 part will be: €300 ÷ 5 = €60
To find Alan's share multiply €60 x 3 = €180
John's share is €60 x 2 = €120

## Slide 7: Using ratios to solve problems
Q1. A batch of concrete has been mixed in the ratio of 2 : 5 : 8 (cement : sand : gravel)
The total weight of the dry mix is 825Kg
Calculate the weight of each part.
Answer
2 + 5 + 8 = 15 825 ÷ 15 = 55
Cement : 2 parts 2 x 55 = 110Kg
Sand : 5 parts 5 x 55 = 275Kg
Gravel : 8 parts 8 x 55 = 440Kg

## Slide 8: Using ratios to solve problems
Q2. A batch of concrete has been mixed in the ratio of 1.5 : 5 : 4 (cement : sand : gravel)
The total weight of the weight mix is 630Kg. One fifth of the total weight is water.
Calculate the weight of each of the 4 parts.
Answer
(1.5 : 5 : 4) x 2 = 3 : 10 : 8 = 21 parts
Find the weight of the water 630 ÷ 5 = Water weighs 126Kg
Subtract the weight of the water 630 – 126 = 504Kg
504 ÷ 21 = 24 1 part = 24Kg
Cement : 3 parts 24 x 3 = 72Kg
Sand : 10 parts 24 x 10 = 240Kg
Gravel : 8 parts 24 x 8 = 192Kg